Notes on DJI OSDK

## Attitude control / velocity control
- Position control using only attitude control and z velocity/position seems possible
  - Use the functions from dji_control.cpp/hpp to achieve this
  - Commands must be sent continuously or else it will switch to position hold (GPS or attitude if no GPS I guess??)
    - How fast needs to be tested but seems like faster than 3 Hz
  - I would presume that this is possible even when GPS is not available
- Takeoff (auto/buildin) uses GPS for positioning and flies to ~1m before anything else can be done.
  - Takeoff can be done using the position/speed controls instead so full control is maintained during takeoff
- Also has position and velocity control options but these are based on the world frame
  - Seems to be GPS dependent
    - Only tested in simulator (perfect GPS signal)
  - World frame is always NED (North-East-Down)

## Virtual RC
- Virtual RC can be used by simulating a RC giving stick values to the craft
  - Needed to change dji_command.cpp initialization of the cmd_id
  - Need to obtain control authority after use to use OSDK to control. Else it gives a controller fail
  - Max roll/pitch is 35 deg instead 30 as when using controller(RC)
  - Works like regular controller in the given mode (P, A) (and F??)
  - Can arm/disarm and takeoff / land using this.

## Autnav controller
- Autnav controller is compatible with the matrice 100 in the simulation
- Simulated with GPS as global reference
- In ideal conditions model seems to fit very good with the simulator model
- Can be run at 400Hz with all the desired information available
- Global coordinate system are not the same so needs to be accounted for if matrice global position is to be used. (If all in camera/laserscanner this is no problem as we define these)
- Z velocity control is available so a height controller could be added to autnav (so it is only rangefinder based)
  - Depends on how it works in GPS denied areas
- Should be created to run in a controller thread to ensure timings and reliable updates